## Slide 1: Introduction to Stage Lighting
Kunwu Lyu
20240928
https://github.com/kwlyu/EOS-Training

## Slide 2: Topics to Cover
Setup
Cue Writing Basics
  Patch, Channel, Parameters, Groups, Cues, Playback, Update
Workspace Navigation
  Display Layouts, Palettes and Presets, Direct Selects
Intro Effects
  Macros, Fan and Offset, Effects
Show Control
  Timecode Integration with REAPER and QLab

## Slide 3: Goal
Give me something cool?

## Slide 4: Patching
[21] [Thru] [29] [Enter]
Click on {Type} in the lower right hand corner of display
Click on {Search}
Find {ETC Fixtures} in left columns
Then {D40 Lustr+ HIS Str +7}

## Slide 5: Channel vs Address
A channel can be
  A dimmer
  Multiple dimmers
  Color-changing LEDs fixture
  One Moving Light
  A Source Four with a Color Scroller
An address can be
  A dimmer
  One parameter of a moving light
  One parameter or color of an LED fixture

## Slide 6: Types of Fixtures
FLOODLIGHT
  Cover a large area at a relatively short throw distance. Lighting scenic cloths and cycloramas.
PAR
  Create very bright, intense beams of light and can be used to create washes of color and striking beam effects.

## Slide 7: Types of Fixtures (cont.)
FRESNEL
  Produce a soft-edged beam of light and can be used to create even washes of light on stage by adjusting the beam angle from a narrow spot to a wide flood. Using ‘barndoors’, you can also roughly shape and contain the light
PROFILE
  Also called ‘Ellipsoidals.’ Available in a variety of beam angles, profiles are capable of projecting hard- or soft-edged beams of light and have a set of internal shutters that allow you to precisely shape the beam. They can also project patterns or ‘gobos’ to cast window projections or other textured effects. Followspots fall into this category

## Slide 8: Types of Fixtures
MOVING LIGHTS
  Moving lights are just automated versions of the above types of lights. Moving lights are typically broken down into two types – spots and washes. Wash lights are automated versions of the PAR or Fresnel, and Spots are automated versions of Profiles.

## Slide 9: A Word on the Stage

## Slide 10: Patching Exercise

## Slide 11: Channels in Live
Hold [Tab], Press [1], Release [Tab]
[201] [Thru] [219] [At] [5] [Enter]
  sets level of 50% (use [05] for 5%)
[Clear] [Sneak] [Enter]
  restores all manual levels to background states

## Slide 12: Parameters

## Slide 13: Groups
A channel selection tool used for fast recall of specific channels
[21] [Thru] [29] [Record] [Group] [21] [Enter]
  Records channels to the target group
[Group] [21] {Offset} {Mirror Out} [Record] [Group] [25] [Enter]
  Using Offset to achieve center-out
[Group] [21] [At] [20] [Thru] [Full] [Enter]
  Fanned intensity but in order this time

## Slide 14: Cues
Single lighting looks that are stored in a list and often played back in order
[Clear] [Sneak] [Enter]
[Group] [200] [+] [91] [+] [21] [At] [5] [Enter]
[Select Last]
Select Color
[Record] [2] [Time] [3] [Enter]
[Label] B/O [Enter]

## Slide 15: Color Conventions

## Slide 16: Cue Writing Exercise #1
Make anything your Cue 3
It has to involve non-intensity parameters
Call it Stage Up

## Slide 17: Cue Follow/Hang (Auto-Follows)
An auto-follow is when one cue automatically activates the next cue.
Follow time begins the moment the cue is executed (when the go button is pressed.)
Hang is similar but doesn’t start till the cue is complete.
{Fw/Hg} is a soft key; can also press [Shift] & [Delay] to access Follow and [Shift] & [Delay] [Delay] to access Hang

## Slide 18: Cue Writing Exercise #2
Make a 2-step “Pulse” Cue with Follow/Hang

## Slide 19: Playback
PSD is a tab that displays a list of the cues, their timing and additional information associated with the cues.
Press (Go)
  Hold [Shift] and Press(Go)
Press (Stop/Back)
  Hold [Shift] and Press(Stop/Back)
[Go To Cue] [3] [Enter]
  [Go To Cue] [1] [Time] [1] [Enter]

## Slide 20: Update
Update is a “save changes” tool. It only pertains to values that are red or modified – values that have been changed.
[Update] [Cue Only] [Enter]
  Records without tracking

## Slide 21: Display Layouts and Workspaces
Snapshots store layouts so that you can recall them quickly. They are stored in the show file, can be recalled on any device on the network.
[Record] [{Snapshot}] [3] [Enter]
[{Snapshot}] [3] [Enter]

## Slide 22: Palettes
Four types of palettes that correspond with the four data categories – Intensity, Focus, Color, and Beam
[Group] [21] [Full] [Enter] {Color Picker} and select a red
[Select Last] [Record] [Color Palette] [21] [Label] Dk Red [Enter]

## Slide 23: Presets --- All Palettes
Presets can collect all data for a given channel (intensity, focus, color, and beam palettes as well as absolute data) rather than just one parameter type like with a palette.
Fly In ----- Up (FP) and Off (IP) -> Down and On
Fly Out --- Down and Off -> Up and Off

## Slide 24: Direct Selects

## Slide 25: Macros
A Macro is an automated series of console actions. Macros are a way to automate repetitive, complex or hard-to-reach commands in the desk
[Macro] [Macro]
  Macro Editor Display
[Learn] [4] [Enter] {Allow App Connections} [Learn]

## Slide 26: Effects!
Four Type of Basic Effects
Step
Sine
Burst
Ramp

## Slide 27: A Word on Numbers

## Slide 28: Timecode!
Show Control